## Slide 1: Z-Wave Overview
2020

## Slide 2
16°C
Z-Wave Home
Gateway

## Slide 3: What’s Z-Wave
allowing for wireless control of residential appliances and other devices, such as lighting control, security systems, thermostats, windows, locks.
Z-Wave provides the application layer interoperability between home control systems of different manufacturers that are a part of its alliance.
Z-Wave is a wireless communications protocol used primarily for home automation.
Mesh, Low energy, Low rate, Short range
Home Automation
Interoperability

## Slide 4: Z-Wave PHY
Sub GHz, license free ISM bands, region/Country specific
Data rate \ region frequency & channel(s) | US / Canada / South America | EU / UAE / China / India | AU / NZ / Brazil | Japan / Taiwan / Korea / Singapore
9.6kbps FSK Modulation | 908 MHz Ch 1 | 868 MHz Ch 1 | 921 MHz Ch 1 | NA
40kpbs FSK Modulation | 908 MHz Ch 1 | 868 MHz Ch 1 | 921 MHz Ch 1 | NA
100kpbs GFSK Modulation | 916 MHZ Ch 2 | 869 MHz Ch 2 | 919 MHz Ch 2 | 919-926 MHz Ch 1 - 3
https://www.silabs.com/products/wireless/mesh-networking/z-wave/benefits/technology/global-regions
Z-Wave Global Regions

## Slide 5: Singlecast Example
Singlecast
Acknowledgment
(if Transfer w/ ACK)
    Transmission from a Node to another Node
    Transfer Acknowledge is sent as reply
Frame Types
Broadcast frames
Multicast frames
Singlecast frames

## Slide 6: Z-Wave Device Archetypes
·
Notes: z-wave网络定义了两种设备原型。controller和slave
或者叫end device

## Slide 7: Z-wave Device Role types
Mains powered
  Always On Slave [AOS]
Battery powered
  Reporting Sleeping Slave [RSS]
  Listening Sleeping Slave [LSS]

## Slide 8: Always On Slave [AOS]
Always ON devices
Must be mains powered
Always reachable
  Can receive and send commands at all times
The back-bone of the Z-Wave mesh
  Is a repeater in the network

## Slide 9: Z-Wave Route Rule
Explorer Frames
Special class of the broadcast frame that enables dynamic routing
It is used to discover/rediscover routes
Application command is included in the explorer frame
Explorer Frame Response
Explorer response uses source routing
Becomes the LWR when received
Limitation
4 seconds timeout
Only be sent to always on devices
Limits the maximum payload
Explorer frame
Search result frame
Explorer Frames

## Slide 10: Z-Wave Device Inclusion/Exclusion
The business card of the Z-Wave node
Announces protocol and Application level capabilities
Network capabilities of the device
Device Classes implemented
List of Command Classes supported
Optionally - List of Command Classes controlled
The Node Information Frame [NIF]

## Slide 11: Interoperability & Command class
Interoperability is required of all Z-Wave devices.
For the device to achieve Z-Wave interoperability the product must pass the Z-Wave Certification program
Only certified Z-Wave devices may carry the Z-Wave or Z-Wave Plus logo.
There are no proprietary implementation or closed ecosystems / walled-gardens with Z-Wave. All devices must coexist and allow usage of the device or devices regardless of make, model, or manufacturer.
Required
Z-Wave Certification
Z-Wave logo
Coexist
More Importantly, Interoperability is Required

## Slide 12: Interoperability & Command class
  The device is well described:
  Role Device Class
  Defines the role in the network.
  Device Classes
  Describes the type and functionality of a device.
  Command classes
  The grammar for the Z-Wave language.
How does Z-Wave ensure Interoperability?
Welcome to the network.
I’m a Controller.
I’m an Always-On-Slave